## Slide 1: Systematic Review of JSATS Passage and Survival Data at Bonneville and The Dalles Dams during Alternate Turbine and Spillbay Operations from 2008-2012
Mark Weiland, Bishes Rayamajhi, Jina Kim, Christa Woodley, Gene Ploskey, Jon Rerecich1 AND Brad Eppard1
Pacific Northwest National Laboratory
1U.S. Army Corps of Engineers, Portland District, Portland, OR
Notes: Good morning?. At this time I’d like to acknowledge my co-authors and thank the Corp for funding this study. I would also like to acknowledge a lot of other people were involved with the acquisition of this data and specifically acknowledge Katie Wagner who helped with data QC and Tao Fu for helping pull the data together.
Studies using JSATS have been conducted at dams on the LCR for a number of years to evaluate behavior at time of passage and survival of juvenile salmonids for the BiOp. Studies were conducted at Bonneville Dam from 2008-2012 and from 2010-2012 at the Dalles Dam. The results I’ll be presenting today are an integration of this data across years to increase sample sizes and to provide a picture across a larger range of operating and environmental conditions that normally aren’t seen within individual years to determine the best operating conditions at Bonneville Dam powerhouses 1 and 2, the spillway; and at the TDA spillway to determine if survival is lower when fish pass outside of the spillway wall when additional bays need to be opened during high flow events.

## Slide 2: Introduction: BON
Operation of Bonneville Dam to reduce fish injury
  B2 operation at low to mid range of 1% peak efficiency
    Improve conditions for guided fish in the gatewell
    May result in unfavorable conditions for turbine passed fish
  B1 increase flow to offset reduced discharge at B2
    Compare survival within to above the 1% operating range
      Best operating point (range) as identified by TSP
  Spillway survival variability
    Erosion of stilling basin or ogees in several spill bays and accumulation of rock
Notes: The Corp has been working to determine the best turbine operating ranges and spill patterns for survival of juvenile salmonids passing Bonneville Dam. Due to increased injury and mortality of juvenile salmonids in the gatewell’s of the Second Powerhouse (B2) at high discharge, turbines at B2 have been operated more frequently at the lower to mid range of the 1% peak efficiency range translating to reduced hydraulic capacity at this powerhouse. This operation is better for guided fish but may create conditions in the turbine environment that decreases fish survival.
Due to reduced discharge at B2 more flow is then diverted to B1.
The Turbine Survival Program has been working to identify the best operating point for turbine units at each project that reduces the probability of mortal injury for fish. These modeling studies have indicated that operation of turbine units at an open geometry configuration (i.e. alignment of wicket gates and stay vanes) improves hydraulic conditions in the turbine environment that may improve passage survival for fish. At the First Powerhouse (B1) it was determined that the best operating point is above the upper limit of the 1% peak efficiency range. It has been recommended that until gatewell hydraulic conditions at are resolved flow in excess of B2 capacity be diverted to B1 and that B1 units operate up to the best operating point. Once B1 capacity is exceeded additional flow is diverted to the spillway.
At the spillway erosion of the structure and rock accumulation may be reducing passage survival, specifically at certain bays.

## Slide 3: Objectives: BON
Analyze 2008-2012 JSATS and operations data to examine survival rates for juvenile salmonids at BON
  B2 Turbine Survival Comparison:
    Examine survival for fish passing turbines operating across the 1% peak efficiency range
  B1 Turbine Survival Comparison:
    Examine survival for fish passing turbines operating within the 1% peak efficiency range and above the upper limit of the 1% operating range
  Bonneville Spillway:
    Examine spillway survival by spillbay with focus on those bays where erosion of the ogee or stilling basin immediately downstream had occurred
Notes: For Bonneville Dam the objectives, were at B1 to analyze data to evaluate survival rates of juvenile salmonids using 2010-2012 data to estimate survival over the range of operating conditions, specifically to determine if survival above the 1% operating range is as good or better than within the 1% peak efficiency range.
At B2 compare turbine passage survival for fish passing turbine over the operating range of the turbines.
At the spillway survival was estimated by bay to determine if there was disproportionate survival across the spillway to determine if erosion of the spillway could be reducing survival. We also grouped this data across multiple bays.

## Slide 4: Methods: BON
B1 turbines
  Lower quarter of 1% efficiency (Q1)
  Lower middle quarter of 1% efficiency (Q2)
  Upper middle quarter of 1% efficiency (Q3)
  1% of peak efficiency (Q4)
  Best operating point/range (BOP)
  Above best operating point to generator limit (ABOP)
B2 turbines
  Lower quarter of 1% efficiency (Q1)
  Lower middle quarter of 1% efficiency (Q2)
  Upper middle quarter of 1% efficiency (Q3)
  1% of peak efficiency (Q4)
BON spillway
  By bay
  Group bays

## Slide 5: Methods: B1 and B2 Binned Operating Ranges
Chart: B1 Turbine Operating Range
| 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64
Best Op Point | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340
Chart: B2 Turbine Operating Range (w/STS)
| 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
UL_Q4 = UL_1% | 18068 | 18097 | 18121 | 18139 | 18153 | 18162 | 18197 | 18228 | 18255 | 18278 | 18299 | 18366 | 18200 | 18040 | 17887 | 18598 | 18850 | 19091 | 19323 | 19536 | 19115 | 18718 | 18336 | 17967 | 17611 | 17267 | 16978 | 16699 | 16428 | 16166 | 15912 | 15671 | 15437 | 15210 | 14990 | 14775
UL_Q3 | 16365.75 | 16390.5 | 16410.5 | 16425.25 | 16436.5 | 16443.5 | 16462.5 | 16478.5 | 16491.5 | 16501.5 | 16510.25 | 16559.25 | 16433.75 | 16312.25 | 16196.25 | 16728 | 16926 | 17115 | 17297 | 17464.25 | 17155.75 | 16874.25 | 16603 | 16340.5 | 16087 | 15842 | 15616.5 | 15398.75 | 15187.5 | 14983 | 14785.25 | 14615.25 | 14450.25 | 14290.5 | 14135.25 | 13983.75
UL_Q2 | 14663.5 | 14684 | 14700 | 14711.5 | 14720 | 14725 | 14728 | 14729 | 14728 | 14725 | 14721.5 | 14752.5 | 14667.5 | 14584.5 | 14505.5 | 14858 | 15002 | 15139 | 15271 | 15392.5 | 15196.5 | 15030.5 | 14870 | 14714 | 14563 | 14417 | 14255 | 14098.5 | 13947 | 13800 | 13658.5 | 13559.5 | 13463.5 | 13371 | 13280.5 | 13192.5
UL_Q1 | 12961.25 | 12977.5 | 12989.5 | 12997.75 | 13003.5 | 13006.5 | 12993.5 | 12979.5 | 12964.5 | 12948.5 | 12932.75 | 12945.75 | 12901.25 | 12856.75 | 12814.75 | 12988 | 13078 | 13163 | 13245 | 13320.75 | 13237.25 | 13186.75 | 13137 | 13087.5 | 13039 | 12992 | 12893.5 | 12798.25 | 12706.5 | 12617 | 12531.75 | 12503.75 | 12476.75 | 12451.5 | 12425.75 | 12401.25
LL_Q1 = LL_1% | 11259 | 11271 | 11279 | 11284 | 11287 | 11288 | 11259 | 11230 | 11201 | 11172 | 11144 | 11139 | 11135 | 11129 | 11124 | 11118 | 11154 | 11187 | 11219 | 11249 | 11278 | 11343 | 11404 | 11461 | 11515 | 11567 | 11532 | 11498 | 11466 | 11434 | 11405 | 11448 | 11490 | 11532 | 11571 | 11610

## Slide 6: BON B1 Survival By Species and Operation

## Slide 7: Analyses: BON B1 CH1 Passage Distribution
Chart: HEAD (ft)
| 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64
Best Op Range | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340
Best Op Range
Q4
Q3
Q2
Q1
Above BOR
Chart: 
Chart: 
Chart: 
2010
2011
2012

## Slide 8: Analyses: BON B1 CH1 Survival by Operating Condition
Survival
Survival
Chart: 
Chart: 
| LL to UL | LL to BOP | UL to BOP | ABOP
CH1 | 0.9644 | 0.9648 | 0.9672 | 0.964
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
CR234.0 to CR156.0 | 0.9626 | 0.9971 | 1.0023 | 0.953 | 0.9534

## Slide 9: Analyses: BON B1 STH Passage Distribution
2010
2011
2012
Chart: HEAD (ft)
Best Op Range | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340
Chart: 
Best Op Range
Q4
Q3
Q2
Q1
Above BOR
Chart: 
Chart: 

## Slide 10: Analyses: BON B1 STH Survival by Operating Condition
Chart: 
Survival
Survival
Chart: 
Chart: 
| LL to UL | LL to BOP | UL to BOP | ABOP
STH | 0.9335 | 0.9357 | 0.9477 | 0.9328
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
CR234.0 to CR156.0 | 0.8673 | 0.974 | 0.9173 | 0.9064 | 0.93

## Slide 11: Analyses: BON B1 CH0 Passage Distribution
Chart: HEAD (ft)
Best Op Range | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340
Chart: 
Chart: 
2010
2011
2012
Best Op Range
Q4
Q3
Q2
Q1
Above BOR

## Slide 12: Analyses: BON B1 CH0 Survival by Operating Condition
Survival
Survival
Chart: 
| LL to UL | LL to BOP | UL to BOP | ABOP
CH0 | 0.9534 | 0.953 | 0.9515
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
CR234.0 to CR156.0 | 1 | 0.9362 | 0.9145 | 0.976 | 0.9537

## Slide 13: BON B1 Survival at Lower & Upper BOP

## Slide 14: Analyses: BON B1 CH1 Survival within BOP
Chart: 
| 48.59 | 49.58 | 49.06 | 46.11 | 48.6 | 49.5 | 48.78 | 51.56 | 48.27 | 48.85 | 48.03 | 49.46
VR_B1_T_CH1_UBOP | 10700 | 10700 | 10800 | 10800 | 10900 | 10900 | 10900 | 10900 | 11000 | 11100 | 11100 | 11100
Best Op Point | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340

## Slide 15: Analyses: BON B1 STH Survival within BOP
Chart: 
| 51.67 | 48.99 | 49.05 | 48.92 | 46.02 | 51.56 | 49.87 | 49.64 | 49.74 | 49.89 | 48.59 | 49.78 | 48.53 | 49.58 | 47.7 | 50.77 | 51.18
VR_B1_T_STH_UBOP | 10400 | 10500 | 10700 | 10700 | 10700 | 10900 | 10900 | 11000 | 11000 | 11000 | 11100 | 11100 | 11100 | 11200 | 11200 | 11300 | 11300
Best Op Point | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340

## Slide 16: Analyses: BON B1 CH0 Survival within BOP
Chart: 
Best Op Point | 10627 | 10654 | 10677 | 10759 | 10837 | 10910 | 10979 | 11045 | 11109 | 11170 | 11227 | 11282 | 11333 | 11356 | 11378 | 11398 | 11418 | 11465 | 11478 | 11518 | 11557 | 11594 | 11630 | 11610 | 11591 | 11572 | 11519
UL_Q4 = UL_1% | 8918 | 8886 | 8854 | 8969 | 9077 | 9180 | 9278 | 9370 | 9416 | 9459 | 9500 | 9539 | 9575 | 9618 | 9577 | 9537 | 9499 | 9768 | 9808 | 9846 | 9883 | 9918 | 9952 | 9930 | 9909 | 9889 | 9868
UL_Q3 | 8489.5 | 8465 | 8440.25 | 8527 | 8608.25 | 8685.75 | 8759.25 | 8828.25 | 8864.5 | 8898.5 | 8930.75 | 8961.5 | 8989.75 | 9023.75 | 8994.75 | 8966.25 | 8939.25 | 9142.5 | 9173.25 | 9202.5 | 9230.75 | 9257.75 | 9283.75 | 9271.5 | 9259.5 | 9248.25 | 9236
UL_Q2 | 8061 | 8044 | 8026.5 | 8085 | 8139.5 | 8191.5 | 8240.5 | 8286.5 | 8313 | 8338 | 8361.5 | 8384 | 8404.5 | 8429.5 | 8412.5 | 8395.5 | 8379.5 | 8517 | 8538.5 | 8559 | 8578.5 | 8597.5 | 8615.5 | 8613 | 8610 | 8607.5 | 8604
UL_Q1 | 7632.5 | 7623 | 7612.75 | 7643 | 7670.75 | 7697.25 | 7721.75 | 7744.75 | 7761.5 | 7777.5 | 7792.25 | 7806.5 | 7819.25 | 7835.25 | 7830.25 | 7824.75 | 7819.75 | 7891.5 | 7903.75 | 7915.5 | 7926.25 | 7937.25 | 7947.25 | 7954.5 | 7960.5 | 7966.75 | 7972
LL_Q1 = LL_1% | 7204 | 7202 | 7199 | 7201 | 7202 | 7203 | 7203 | 7203 | 7210 | 7217 | 7223 | 7229 | 7234 | 7241 | 7248 | 7254 | 7260 | 7266 | 7269 | 7272 | 7274 | 7277 | 7279 | 7296 | 7311 | 7326 | 7340
Above BOP
Best Op Point
Q4
Q3
Q2
Q1

## Slide 17: BON B2 Survival By Species and Operation

## Slide 18: Analyses: BON B2 CH1 Passage by Quartile
Q4
Q3
Q2
Q1
2008
2009
2010
2011
2012
Chart: HEAD (ft)
| 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
UL_Q4 = UL_1% | 18068 | 18097 | 18121 | 18139 | 18153 | 18162 | 18197 | 18228 | 18255 | 18278 | 18299 | 18366 | 18200 | 18040 | 17887 | 18598 | 18850 | 19091 | 19323 | 19536 | 19115 | 18718 | 18336 | 17967 | 17611 | 17267 | 16978 | 16699 | 16428 | 16166 | 15912 | 15671 | 15437 | 15210 | 14990 | 14775
UL_Q3 | 16365.75 | 16390.5 | 16410.5 | 16425.25 | 16436.5 | 16443.5 | 16462.5 | 16478.5 | 16491.5 | 16501.5 | 16510.25 | 16559.25 | 16433.75 | 16312.25 | 16196.25 | 16728 | 16926 | 17115 | 17297 | 17464.25 | 17155.75 | 16874.25 | 16603 | 16340.5 | 16087 | 15842 | 15616.5 | 15398.75 | 15187.5 | 14983 | 14785.25 | 14615.25 | 14450.25 | 14290.5 | 14135.25 | 13983.75
UL_Q2 | 14663.5 | 14684 | 14700 | 14711.5 | 14720 | 14725 | 14728 | 14729 | 14728 | 14725 | 14721.5 | 14752.5 | 14667.5 | 14584.5 | 14505.5 | 14858 | 15002 | 15139 | 15271 | 15392.5 | 15196.5 | 15030.5 | 14870 | 14714 | 14563 | 14417 | 14255 | 14098.5 | 13947 | 13800 | 13658.5 | 13559.5 | 13463.5 | 13371 | 13280.5 | 13192.5
UL_Q1 | 12961.25 | 12977.5 | 12989.5 | 12997.75 | 13003.5 | 13006.5 | 12993.5 | 12979.5 | 12964.5 | 12948.5 | 12932.75 | 12945.75 | 12901.25 | 12856.75 | 12814.75 | 12988 | 13078 | 13163 | 13245 | 13320.75 | 13237.25 | 13186.75 | 13137 | 13087.5 | 13039 | 12992 | 12893.5 | 12798.25 | 12706.5 | 12617 | 12531.75 | 12503.75 | 12476.75 | 12451.5 | 12425.75 | 12401.25
LL_Q1 = LL_1% | 11259 | 11271 | 11279 | 11284 | 11287 | 11288 | 11259 | 11230 | 11201 | 11172 | 11144 | 11139 | 11135 | 11129 | 11124 | 11118 | 11154 | 11187 | 11219 | 11249 | 11278 | 11343 | 11404 | 11461 | 11515 | 11567 | 11532 | 11498 | 11466 | 11434 | 11405 | 11448 | 11490 | 11532 | 11571 | 11610
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 19: Analyses: BON B2 CH1 Survival by Operating Condition
Survival
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
 | 0.9167 | 0.9545 | 0.9575 | 0.9501 | 0.9563

## Slide 20: Analyses: BON B2 STH Passage Distribution
2008
2009
2010
2011
2012
Q4
Q3
Q2
Q1
Chart: HEAD (ft)
| 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
UL_Q4 = UL_1% | 18068 | 18097 | 18121 | 18139 | 18153 | 18162 | 18197 | 18228 | 18255 | 18278 | 18299 | 18366 | 18200 | 18040 | 17887 | 18598 | 18850 | 19091 | 19323 | 19536 | 19115 | 18718 | 18336 | 17967 | 17611 | 17267 | 16978 | 16699 | 16428 | 16166 | 15912 | 15671 | 15437 | 15210 | 14990 | 14775
UL_Q3 | 16365.75 | 16390.5 | 16410.5 | 16425.25 | 16436.5 | 16443.5 | 16462.5 | 16478.5 | 16491.5 | 16501.5 | 16510.25 | 16559.25 | 16433.75 | 16312.25 | 16196.25 | 16728 | 16926 | 17115 | 17297 | 17464.25 | 17155.75 | 16874.25 | 16603 | 16340.5 | 16087 | 15842 | 15616.5 | 15398.75 | 15187.5 | 14983 | 14785.25 | 14615.25 | 14450.25 | 14290.5 | 14135.25 | 13983.75
UL_Q2 | 14663.5 | 14684 | 14700 | 14711.5 | 14720 | 14725 | 14728 | 14729 | 14728 | 14725 | 14721.5 | 14752.5 | 14667.5 | 14584.5 | 14505.5 | 14858 | 15002 | 15139 | 15271 | 15392.5 | 15196.5 | 15030.5 | 14870 | 14714 | 14563 | 14417 | 14255 | 14098.5 | 13947 | 13800 | 13658.5 | 13559.5 | 13463.5 | 13371 | 13280.5 | 13192.5
UL_Q1 | 12961.25 | 12977.5 | 12989.5 | 12997.75 | 13003.5 | 13006.5 | 12993.5 | 12979.5 | 12964.5 | 12948.5 | 12932.75 | 12945.75 | 12901.25 | 12856.75 | 12814.75 | 12988 | 13078 | 13163 | 13245 | 13320.75 | 13237.25 | 13186.75 | 13137 | 13087.5 | 13039 | 12992 | 12893.5 | 12798.25 | 12706.5 | 12617 | 12531.75 | 12503.75 | 12476.75 | 12451.5 | 12425.75 | 12401.25
LL_Q1 = LL_1% | 11259 | 11271 | 11279 | 11284 | 11287 | 11288 | 11259 | 11230 | 11201 | 11172 | 11144 | 11139 | 11135 | 11129 | 11124 | 11118 | 11154 | 11187 | 11219 | 11249 | 11278 | 11343 | 11404 | 11461 | 11515 | 11567 | 11532 | 11498 | 11466 | 11434 | 11405 | 11448 | 11490 | 11532 | 11571 | 11610
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 21: Analyses: BON B2 STH Survival by Operating Condition
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
CR234.0 to CR156.0 | 1.0214 | 0.8932 | 0.9427 | 0.9097 | 0.9192
Survival

## Slide 22: Analyses: BON B2 CH0 Passage Distribution
2008
2009
2010
2011
2012
Q4
Q3
Q2
Q1
Chart: HEAD (ft)
| 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
UL_Q4 = UL_1% | 18068 | 18097 | 18121 | 18139 | 18153 | 18162 | 18197 | 18228 | 18255 | 18278 | 18299 | 18366 | 18200 | 18040 | 17887 | 18598 | 18850 | 19091 | 19323 | 19536 | 19115 | 18718 | 18336 | 17967 | 17611 | 17267 | 16978 | 16699 | 16428 | 16166 | 15912 | 15671 | 15437 | 15210 | 14990 | 14775
UL_Q3 | 16365.75 | 16390.5 | 16410.5 | 16425.25 | 16436.5 | 16443.5 | 16462.5 | 16478.5 | 16491.5 | 16501.5 | 16510.25 | 16559.25 | 16433.75 | 16312.25 | 16196.25 | 16728 | 16926 | 17115 | 17297 | 17464.25 | 17155.75 | 16874.25 | 16603 | 16340.5 | 16087 | 15842 | 15616.5 | 15398.75 | 15187.5 | 14983 | 14785.25 | 14615.25 | 14450.25 | 14290.5 | 14135.25 | 13983.75
UL_Q2 | 14663.5 | 14684 | 14700 | 14711.5 | 14720 | 14725 | 14728 | 14729 | 14728 | 14725 | 14721.5 | 14752.5 | 14667.5 | 14584.5 | 14505.5 | 14858 | 15002 | 15139 | 15271 | 15392.5 | 15196.5 | 15030.5 | 14870 | 14714 | 14563 | 14417 | 14255 | 14098.5 | 13947 | 13800 | 13658.5 | 13559.5 | 13463.5 | 13371 | 13280.5 | 13192.5
UL_Q1 | 12961.25 | 12977.5 | 12989.5 | 12997.75 | 13003.5 | 13006.5 | 12993.5 | 12979.5 | 12964.5 | 12948.5 | 12932.75 | 12945.75 | 12901.25 | 12856.75 | 12814.75 | 12988 | 13078 | 13163 | 13245 | 13320.75 | 13237.25 | 13186.75 | 13137 | 13087.5 | 13039 | 12992 | 12893.5 | 12798.25 | 12706.5 | 12617 | 12531.75 | 12503.75 | 12476.75 | 12451.5 | 12425.75 | 12401.25
LL_Q1 = LL_1% | 11259 | 11271 | 11279 | 11284 | 11287 | 11288 | 11259 | 11230 | 11201 | 11172 | 11144 | 11139 | 11135 | 11129 | 11124 | 11118 | 11154 | 11187 | 11219 | 11249 | 11278 | 11343 | 11404 | 11461 | 11515 | 11567 | 11532 | 11498 | 11466 | 11434 | 11405 | 11448 | 11490 | 11532 | 11571 | 11610
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 23: Analyses: BON B2 CH0 Survival by Operating Condition
Chart: 
| <1% | Q1 | Q2 | Q3 | Q4
CR234.0 to CR156.0 | 0.6853 | 0.9528 | 0.9314 | 0.9397 | 0.9562
Survival

## Slide 24: B2: STS vs No STS, 2008 & 2011
CH1 |  |  |  | 
 |  | Estimate | s.e. | Count
2008 | With STS_Q4 | 0.9320 | 0.0414 | 69
 | Without STS_Q4 | 0.8299 | 0.0617 | 61
2011 | With STS_Q4 | 0.9414 | 0.0495 | 50
 | Without STS_Q4 | 0.9369 | 0.0601 | 37
 | With STS_Q3_Q4 | 0.9511 | 0.0338 | 125
 | Without STS_Q3_Q4 | 0.9771 | 0.0494 | 50
STH |  |  |  | 
 |  | Estimate | s.e. | Count
2008 | With STS_Q4 | 0.9339 | 0.071 | 29
 | Without STS_Q4 | 1.0417 | 0.2039 | 24
2011 | With STS_Q4 | 0.9000 | 0.0987 | 15
 | Without STS_Q4 | 0.9231 | 0.0739 | 13
 | With STS_Q3_Q4 | 0.8907 | 0.0553 | 45
 | Without STS_Q3_Q4 | 0.9790 | 0.0527 | 22

## Slide 25: BON Spillway Surival

## Slide 26: Analyses: BON Spillway CH1 and STH Survival by Bay
Chart: Yearling Chinook
| Bay01 | Bay02 | Bay03 | Bay04 | Bay05 | Bay06 | Bay07 | Bay08 | Bay09 | Bay10 | Bay11 | Bay12 | Bay13 | Bay14 | Bay15 | Bay16 | Bay17 | Bay18
CR234.0 to CR156.0 Estimate | 0.9344 | 0.9223 | 0.9184 | 0.9395 | 0.9598 | 0.9573 | 0.9412 | 0.9495 | 0.9127 | 0.9503 | 0.9288 | 0.923 | 0.9191 | 0.9572 | 0.9249 | 0.9527 | 0.9303 | 0.9513
Survival
Survival
Chart: Steelhead
| Bay01 | Bay02 | Bay03 | Bay04 | Bay05 | Bay06 | Bay07 | Bay08 | Bay09 | Bay10 | Bay11 | Bay12 | Bay13 | Bay14 | Bay15 | Bay16 | Bay17 | Bay18
Survival CR234.0 to CR156.0 Estimate | 0.9537 | 0.9396 | 0.9231 | 0.9641 | 0.9408 | 0.9224 | 0.9385 | 0.9429 | 0.9338 | 0.9566 | 0.9499 | 0.9602 | 0.9484 | 0.9468 | 0.9573 | 0.9448 | 0.9399 | 0.9525

## Slide 27: Analyses: BON Spillway CH1 and STH Survival, Grouped Bays
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
CR234.0 to CR156.0 | 0.9239 | 0.9488 | 0.9332 | 0.9335 | 0.943
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
CR234.0 to CR156.0 | 0.9377 | 0.9438 | 0.949 | 0.9512 | 0.9453
Survival
Survival
Steelhead
Yearling Chinook

## Slide 28: Analyses: BON Spillway Survival by Grouped Bays
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
2008 | 0.9659 | 0.9631 | 0.9491 | 0.9345 | 0.9472
2010 | 0.9042 | 0.9522 | 0.9437 | 0.9204 | 0.9427
2011 | 0.9309 | 0.9469 | 0.9242 | 0.9447 | 0.9591
2012 | 0.9144 | 0.949 | 0.9506 | 0.9424 | 0.9303
Survival
Yearling Chinook
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
2008 | 0.9474 | 0.9728 | 0.966 | 0.9387 | 0.9478
2010 | 0.9197 | 0.9368 | 0.9552 | 0.9428 | 0.951
2011 | 0.9474 | 0.9531 | 0.9439 | 0.9598 | 0.9418
2012 | 0.9267 | 0.927 | 0.9419 | 0.953 | 0.9379
Survival

## Slide 29: Analyses: BON Spillway CH0 Survival by Bay
Chart: CH0
Survival
Chart: Subyearling Chinook
| Bay01 | Bay02 | Bay03 | Bay04 | Bay05 | Bay06 | Bay07 | Bay08 | Bay09 | Bay10 | Bay11 | Bay12 | Bay13 | Bay14 | Bay15 | Bay16 | Bay17 | Bay18
Survival CR234.0 to CR156.0 Estimate | 0.9575 | 0.9286 | 0.937 | 0.9596 | 0.9445 | 0.9573 | 0.9374 | 0.9494 | 0.9604 | 0.9739 | 0.9595 | 0.9438 | 0.9552 | 0.956 | 0.9729 | 0.9578 | 0.945 | 0.9422

## Slide 30: Analyses: BON Spillway CH0 Survival, Grouped Bays
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
CR234.0 to CR156.0 | 0.9403 | 0.952 | 0.9577 | 0.9625 | 0.9492
Survival

## Slide 31: Analyses: BON Spillway Survival by Bays, CH0
Chart: CH0
Chart: 
| Bay01-03 | Bay04-07 | Bay08-12 | Bay13-15 | Bay16-18
2008 | 0.9506 | 0.9263 | 0.9601 | 0.9567 | 0.9574
2010 | 0.9211 | 0.9377 | 0.9369 | 0.9385 | 0.9234
2012 | 0.9452 | 0.9643 | 0.9643 | 0.9722 | 0.9575
Survival

## Slide 32: Analyses: BON Spillway CH1 and STH Survival by Discharge
Chart: 
| <=90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | >=290
CH1 : CR234 to CR156 | 0.9404 | 0.933 | 0.9491 | 0.9481 | 0.9643 | 0.9127 | 0.9603 | 0.9372 | 0.9685 | 0.9308 | 0.9365 | 0.9588 | 0.9165 | 0.9793 | 0.9515 | 0.9541 | 1.0002 | 0.9553 | 0.953 | 0.9752 | 0.8563
% SPW OPS | 0.091494 | 0.35712 | 0.025654 | 0.036569 | 0.042847 | 0.038975 | 0.10276 | 0.013847 | 0.029845 | 0.026913 | 0.026833 | 0.045158 | 0.013767 | 0.013225 | 0.0067402 | 0.0098474 | 0.011552 | 0.012142 | 0.010979 | 0.027168 | 0.056566
Survival
Chart: 
| <=90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | >=290
STH : CR234 to CR156 | 0.9559 | 0.9374 | 0.9317 | 0.9378 | 0.9446 | 0.9159 | 0.9302 | 0.9442 | 0.9848 | 0.9415 | 0.9643 | 0.9942 | 0.98 | 0.9604 | 0.9607 | 1.0182 | 0.9906 | 0.9869 | 0.9463 | 0.953 | 0.8448
% SPW OPS | 0.091494 | 0.35712 | 0.025654 | 0.036569 | 0.042847 | 0.038975 | 0.10276 | 0.013847 | 0.029845 | 0.026913 | 0.026833 | 0.045158 | 0.013767 | 0.013225 | 0.0067402 | 0.0098474 | 0.011552 | 0.012142 | 0.010979 | 0.027168 | 0.056566
Survival
Steelhead

## Slide 33: Analyses: BON Spillway CH0 Survival by Discharge
Chart: 
| <=90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230
CH0 : CR234 to CR156 | 0.9141 | 0.9268 | 0.9476 | 0.9358 | 0.9538 | 0.9795 | 0.9783 | 0.9593 | 0.9539 | 0.9712 | 0.99 | 0.9684 | 0.9845 | 0.9729 | 0.9775
% SPW OPS | 0.30101 | 0.15084 | 0.065088 | 0.075039 | 0.10821 | 0.055577 | 0.08492 | 0.052701 | 0.061678 | 0.01633 | 0.0037345 | 0.010322 | 0.0046624 | 0.0078634 | 0.002018
Chart: Discharge (kcfs)
| 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230
 | 0.9141 | 0.9268 | 0.9476 | 0.9358 | 0.9538 | 0.9795 | 0.9783 | 0.9593 | 0.9539 | 0.9712 | 0.99 | 0.9684 | 0.9845 | 0.9729 | 0.9775
Survival
Discharge (kcfs)

## Slide 34: BON Survival by Tailwater Elevation

## Slide 35: Analyses: BON B1 Survival by Tailwater Level
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.8575 | 0.9403 | 0.9369 | 0.9468 | 0.9306
B1 % OPS | 0.23212 | 0.065018 | 0.17861 | 0.26054 | 0.26371
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.9868 | 1.0052 | 0.9643 | 0.9635 | 0.9652
B1 % OPS | 0.23212 | 0.065018 | 0.17861 | 0.26054 | 0.26371
Yearling Chinook
Survival
Steelhead
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.9868 | 1.0378 | 0.9358
6m | 1.0052 | 1.0350 | 0.9754
7m | 0.9643 | 0.9800 | 0.9486
8m | 0.9635 | 0.9766 | 0.9504
≥ 9m | 0.9652 | 0.9915 | 0.9389
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.8605 | 0.9479 | 0.7731
6m | 0.9480 | 0.9796 | 0.9164
7m | 0.9392 | 0.9572 | 0.9212
8m | 0.9462 | 0.9613 | 0.9311
≥ 9m | 0.9318 | 0.9571 | 0.9065
Survival
Time at TWEL
Time at TWEL

## Slide 36: Analyses: BON B1 Survival by Tailwater Level
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.8939 | 0.9811 | 0.9604 | 0.9517 | 0.9483
B1 % OPS | 0.27255 | 0.053895 | 0.28959 | 0.32536 | 0.05861
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.8939 | 0.9537 | 0.8341
6m | 0.9811 | 1.0070 | 0.9552
7m | 0.9604 | 0.9776 | 0.9432
8m | 0.9517 | 0.9668 | 0.9366
≥ 9m | 0.9483 | 0.9816 | 0.9150
Survival
Sub-Yearling Chinook
Time at TWEL

## Slide 37: Analyses: BON B2 Survival by Tailwater Level
Survival
Survival
Time at TWEL
Time at TWEL
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.8960 | 0.9278 | 0.8642
6m | 0.8955 | 0.9288 | 0.8622
7m | 0.9846 | 1.0052 | 0.9640
8m | 0.8953 | 0.9378 | 0.8528
≥ 9m | 0.9144 | 0.9775 | 0.8513
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.9515 | 0.9750 | 0.9280
6m | 0.9510 | 0.9718 | 0.9302
7m | 0.9577 | 0.9777 | 0.9377
8m | 0.9598 | 0.9776 | 0.9420
≥ 9m | 0.9167 | 0.9602 | 0.8732
Yearling Chinook
Steelhead
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.9515 | 0.951 | 0.9577 | 0.9598 | 0.9167
B2 % OPS | 0.11617 | 0.16425 | 0.15683 | 0.27045 | 0.2923
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.896 | 0.8955 | 0.9846 | 0.8953 | 0.9144
B2 % OPS | 0.11617 | 0.16425 | 0.15683 | 0.27045 | 0.2923

## Slide 38: Analyses: BON B2 Survival by Tailwater Level
Bin | S. Estimate | +95 CI | -95 CI
≤ 5m | 0.9102 | 0.9412 | 0.8792
6m | 0.9440 | 0.9712 | 0.9168
7m | 0.9454 | 0.9685 | 0.9223
8m | 0.9522 | 0.9640 | 0.9404
≥ 9m | 0.9663 | 0.9867 | 0.9459
Survival
Time at TWEL
Sub-Yearling Chinook
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.9102 | 0.944 | 0.9454 | 0.9522 | 0.9663
B2 % OPS | 0.281 | 0.15367 | 0.16874 | 0.32623 | 0.07037

## Slide 39: Analyses: BON Spillway Survival by Tailwater Level
Survival
Survival
Bin | S. Estimate | + 95 CI | -95 CI
≤ 5m | 0.9328 | 0.9477 | 0.9179
6m | 0.9535 | 0.9672 | 0.9398
7m | 0.9302 | 0.9435 | 0.9169
8m | 0.9351 | 0.9474 | 0.9228
≥ 9m | 0.9542 | 0.9726 | 0.9358
Bin | S. Estimate | + 95 CI | -95 CI
≤ 5m | 0.9466 | 0.9635 | 0.9297
6m | 0.9538 | 0.9687 | 0.9389
7m | 0.9311 | 0.9452 | 0.9170
8m | 0.9308 | 0.9433 | 0.9183
≥ 9m | 0.9534 | 0.9683 | 0.9385
Time at TWEL
Time at TWEL
Yearling Chinook
Steelhead
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.9328 | 0.9535 | 0.9302 | 0.9351 | 0.9542
SPW % OPS | 0.14064 | 0.14486 | 0.16132 | 0.27124 | 0.28195
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
CR234.0 to CR156.0 | 0.9466 | 0.9538 | 0.9311 | 0.9308 | 0.9534
SPW % OPS | 0.14064 | 0.14486 | 0.16132 | 0.27124 | 0.28195

## Slide 40: Analyses: BON Spillway Survival by Tailwater Level
Chart: 
| ≤ 5m | 6m | 7m | 8m | ≥ 9m
S CR234.0 to CR156.0 | 0.905 | 0.921 | 0.9508 | 0.9672 | 0.9709
SPW % OPS | 0.19899 | 0.094565 | 0.33713 | 0.35107 | 0.018248
Bin | S. Estimate | + 95 CI | -95 CI
≤ 5m | 0.9050 | 0.9234 | 0.8866
6m | 0.9210 | 0.9418 | 0.9002
7m | 0.9508 | 0.9598 | 0.9418
8m | 0.9672 | 0.9729 | 0.9615
≥ 9m | 0.9709 | 0.9872 | 0.9546
Survival
Time at TWEL
Sub-Yearling Chinook

## Slide 41: BON Egress

## Slide 42: BON: CH1 Tailrace Egress B1 and B2
BON ROUTE | Treatment | Mean | StdErr | Min | Max | Median | N
B1 | ABO | 4.23 | 0.70 | 0.21 | 200.41 | 0.30 | 485
 | BOP | 5.90 | 1.67 | 0.24 | 281.36 | 0.37 | 286
 | Q4 | 3.55 | 0.57 | 0.24 | 273.35 | 0.37 | 860
 | Q3 | 2.43 | 0.82 | 0.23 | 110.46 | 0.38 | 189
 | Q2 | 3.36 | 1.15 | 0.28 | 102.24 | 0.44 | 136
 | Q1 | 6.40 | 2.10 | 0.27 | 280.27 | 0.46 | 234
 | <1% | 15.43 | 14.73 | 0.25 | 310.11 | 0.53 | 21
B2 | Q4 | 0.65 | 0.03 | 0.25 | 3.41 | 0.55 | 141
 | Q3 | 0.92 | 0.12 | 0.29 | 8.61 | 0.61 | 111
 | Q2 | 0.86 | 0.06 | 0.25 | 15.53 | 0.65 | 350
 | Q1 | 0.77 | 0.04 | 0.28 | 18.53 | 0.65 | 514
 | <1% | 0.93 | 0.35 | 0.58 | 1.28 | 0.93 | 2

## Slide 43: BON: STH Tailrace Egress B1 and B2
BON ROUTE | Treatment | Mean | StdErr | Min | Max | Median | N
B1 | ABO | 15.11 | 2.21 | 0.20 | 415.51 | 0.42 | 476
 | BOP | 23.96 | 3.49 | 0.25 | 404.61 | 0.58 | 282
 | Q4 | 17.14 | 1.39 | 0.24 | 419.08 | 0.52 | 1013
 | Q3 | 7.75 | 2.10 | 0.26 | 225.21 | 0.63 | 146
 | Q2 | 9.84 | 4.57 | 0.25 | 589.93 | 0.57 | 146
 | Q1 | 8.51 | 1.69 | 0.25 | 254.90 | 0.60 | 301
 | <1% | 6.61 | 4.55 | 0.31 | 87.32 | 0.77 | 19
B2 | Q4 | 0.89 | 0.10 | 0.22 | 5.19 | 0.71 | 57
 | Q3 | 1.67 | 0.89 | 0.21 | 70.55 | 0.68 | 79
 | Q2 | 1.16 | 0.14 | 0.22 | 24.13 | 0.71 | 257
 | Q1 | 1.16 | 0.16 | 0.26 | 48.20 | 0.72 | 381
 | <1% | 0.75 | 0.46 | 0.25 | 1.66 | 0.33 | 3

## Slide 44: BON: CH0 Tailrace Egress B1 and B2
BON ROUTE | Treatment | Mean | StdErr | Min | Max | Median | N
B1 | BOP | 4.33 | 0.68 | 0.27 | 127.56 | 0.40 | 363
 | Q4 | 3.81 | 0.68 | 0.24 | 622.50 | 0.40 | 1148
 | Q3 | 1.67 | 0.53 | 0.25 | 44.93 | 0.39 | 116
 | Q2 | 1.22 | 0.56 | 0.32 | 31.24 | 0.44 | 56
 | Q1 | 2.17 | 1.45 | 0.29 | 68.26 | 0.46 | 47
 | <1% | 0.81 | 0.13 | 0.56 | 0.97 | 0.90 | 3
B2 | Q4 | 0.78 | 0.03 | 0.19 | 13.90 | 0.64 | 911
 | Q3 | 2.82 | 2.01 | 0.21 | 530.52 | 0.67 | 263
 | Q2 | 0.85 | 0.05 | 0.22 | 8.03 | 0.71 | 272
 | Q1 | 0.83 | 0.06 | 0.29 | 6.15 | 0.73 | 111
 | <1% | 1.03 | - | - | - | 1.03 | 1

## Slide 45: BON: CH1 Tailrace Egress Spillway
SP10 | Mean | StdErr | Min | Max | Median | N
70 | 0.83 | 0.16 | 0.38 | 3.07 | 0.53 | 18
80 | 1.76 | 1.13 | 0.33 | 306.51 | 0.51 | 271
90 | 0.58 | 0.02 | 0.32 | 5.28 | 0.46 | 418
100 | 0.61 | 0.07 | 0.19 | 157.14 | 0.41 | 2571
110 | 0.63 | 0.18 | 0.29 | 26.45 | 0.39 | 142
120 | 0.40 | 0.01 | 0.26 | 1.18 | 0.37 | 264
130 | 0.37 | 0.01 | 0.26 | 1.27 | 0.35 | 250
140 | 0.36 | 0.01 | 0.26 | 0.73 | 0.34 | 124
150 | 0.33 | 0.00 | 0.23 | 1.08 | 0.32 | 285
160 | 0.32 | 0.00 | 0.24 | 0.51 | 0.31 | 113
170 | 1.71 | 1.40 | 0.25 | 68.85 | 0.30 | 49
180 | 0.30 | 0.00 | 0.23 | 0.52 | 0.30 | 116
190 | 0.42 | 0.12 | 0.22 | 3.77 | 0.30 | 28
200 | 0.32 | 0.02 | 0.20 | 1.18 | 0.28 | 91
210 | 0.28 | 0.02 | 0.13 | 0.60 | 0.26 | 31
220 | 1.51 | 1.04 | 0.22 | 11.68 | 0.26 | 11
230 | 0.30 | 0.02 | 0.01 | 0.61 | 0.26 | 43
240 | 0.40 | 0.08 | 0.01 | 4.09 | 0.27 | 66
250 | 0.41 | 0.09 | 0.02 | 11.04 | 0.28 | 122
260 | 0.29 | 0.01 | 0.01 | 0.94 | 0.27 | 136
270 | 0.29 | 0.02 | 0.02 | 2.11 | 0.27 | 110
280 | 0.29 | 0.01 | 0.01 | 1.14 | 0.28 | 129
290 | 0.26 | 0.02 | 0.01 | 0.61 | 0.26 | 39
300 | 0.27 | 0.04 | 0.01 | 0.70 | 0.28 | 16

## Slide 46: BON: STH Tailrace Egress Spillway
SP10 | Mean | StdErr | Min | Max | Median | N
70 | 0.50 | 0.08 | 0.39 | 0.65 | 0.47 | 3
80 | 0.66 | 0.05 | 0.35 | 7.76 | 0.47 | 163
90 | 1.02 | 0.30 | 0.31 | 91.65 | 0.43 | 355
100 | 0.87 | 0.29 | 0.28 | 614.65 | 0.41 | 2179
110 | 0.40 | 0.01 | 0.29 | 0.95 | 0.38 | 118
120 | 0.49 | 0.05 | 0.27 | 10.18 | 0.36 | 227
130 | 0.40 | 0.02 | 0.26 | 4.97 | 0.35 | 245
140 | 0.34 | 0.01 | 0.25 | 1.05 | 0.32 | 170
150 | 0.53 | 0.07 | 0.23 | 12.13 | 0.31 | 266
160 | 0.36 | 0.02 | 0.25 | 1.78 | 0.31 | 103
170 | 0.88 | 0.35 | 0.22 | 13.22 | 0.31 | 38
180 | 0.45 | 0.08 | 0.11 | 9.45 | 0.30 | 131
190 | 0.56 | 0.18 | 0.22 | 6.35 | 0.29 | 34
200 | 0.54 | 0.21 | 0.05 | 14.68 | 0.29 | 70
210 | 0.28 | 0.02 | 0.19 | 0.53 | 0.25 | 21
220 | 0.27 | 0.03 | 0.19 | 0.38 | 0.23 | 7
230 | 0.40 | 0.07 | 0.10 | 1.81 | 0.31 | 26
240 | 0.32 | 0.02 | 0.11 | 0.98 | 0.28 | 56
250 | 0.30 | 0.02 | 0.01 | 1.32 | 0.29 | 111
260 | 0.33 | 0.02 | 0.02 | 2.15 | 0.29 | 133
270 | 0.55 | 0.22 | 0.03 | 22.94 | 0.31 | 103
280 | 0.31 | 0.02 | 0.01 | 1.73 | 0.29 | 142
290 | 0.32 | 0.03 | 0.03 | 0.70 | 0.29 | 39
300 | 0.30 | 0.05 | 0.01 | 0.53 | 0.33 | 8

## Slide 47: BON: CH0 Tailrace Egress Spillway
SP10 | Mean | StdErr | Min | Max | Median | N
80 | 0.69 | 0.07 | 0.40 | 1.30 | 0.54 | 19
90 | 0.60 | 0.02 | 0.34 | 4.48 | 0.51 | 297
100 | 0.53 | 0.01 | 0.31 | 5.79 | 0.45 | 705
110 | 0.43 | 0.01 | 0.31 | 2.18 | 0.41 | 173
120 | 0.42 | 0.01 | 0.27 | 4.87 | 0.38 | 430
130 | 0.40 | 0.02 | 0.26 | 15.92 | 0.36 | 646
140 | 0.35 | 0.00 | 0.26 | 0.88 | 0.34 | 297
150 | 0.39 | 0.05 | 0.23 | 50.35 | 0.32 | 1049
160 | 0.32 | 0.00 | 0.23 | 1.02 | 0.31 | 702
170 | 0.33 | 0.00 | 0.23 | 1.07 | 0.30 | 631
180 | 1.13 | 0.80 | 0.22 | 217.95 | 0.30 | 271
190 | 0.33 | 0.02 | 0.23 | 1.34 | 0.28 | 98
200 | 0.29 | 0.01 | 0.21 | 0.82 | 0.28 | 149
210 | 0.35 | 0.04 | 0.21 | 4.13 | 0.28 | 126
220 | 0.29 | 0.02 | 0.19 | 4.40 | 0.26 | 242
230 | 0.29 | 0.02 | 0.19 | 1.06 | 0.25 | 78

## Slide 48: Conclusions: BON
B1
  There was not a difference in survival for salmonids passing within the 1% of peak operating efficiency and salmonids passing at operations above the upper 1% operating efficiency
B2
  No difference in survival for CH1 across operating range
  No difference in survival for STH across operating range
  No difference in survival for CH0 across operating range
Spillway
  No obvious bay affect
  Lower survival of CH1 and STH above 290 kcfs discharge
  Trend of lower survival for CH0 at low discharge levels

## Slide 49: Introduction: TDA
Introduction
  High flows forced spill discharge at bays outside the new tailrace spillway wall. Concern of lower survival due to predation
Objective
  Examined spillway passage survival for juvenile salmonids passing on the north (spillbays 1-8) and south (spillbays 9-23) of the new spill wall at TDA
  2010-2012 JSATS datasets
Notes: A new spillway wall was built between spillbays 8 and 9 the guide flow, and fish, downstream along the Washington side of the river to keep them away from the islands and predators on the Oregon side of the river. In 2011 and 2012 during high flows operators were forced to open additional spillbays beyond 1-8, outside of the wall, to pass additional water when the capacity of the powerhouse and spillbays 1-8 was exceeded.

## Slide 50: Analyses: TDA Survival Within and Outside of Spill Wall
Chart: 
| Bay01-08 | Bay09-22
2011 and 2012 CH1 : Bay01-08 (92.52%) Bay09-22 (7.48%) N = 6508 | 0.9568 | 0.9486
count | 6021 | 487
Yearling Chinook
Survival
Survival
Steelhead
Chart: 
| Bay01-08 | Bay09-22
2011 and 2012 STH : Bay01-08 (90.83%) Bay09-22 (9.17%) N = 7260 | 0.9683 | 0.9802
count | 6594 | 666
Chart: 
| Bay01-08 | Bay09-22
2012 CH0 : Bay01-08 (97.28%) Bay09-22 (2.72%) N = 5181 | 0.9549 | 0.965
count | 5040 | 141
Subyearling Chinook
Survival
Bay09-23
Bay09-23
Bay09-23

## Slide 51: Analyses: TDA Survival Outside of Spill Wall, Grouped Bays
Chart: 
| Bay09-12 | Bay13-22
2011 and 2012 STH : Bay09-12 (65.32%) Bay13-22 (34.68%) N = 666 | 0.9813 | 0.9784
count | 435 | 231
Survival
Chart: 
| Bay09-12 | Bay13-22
2011 and 2012 CH1 : Bay09-12 (62.42%) Bay13-22 (37.58%) N = 487 | 0.9472 | 0.9508
count | 304 | 183
Yearling Chinook
Survival
Steelhead
Subyearling Chinook
Survival
Bay13-23
Bay13-23
Bay13-23

## Slide 52: Analyses: TDA Survival Grouped by Flow
Chart: 
| <=72k | 96k | 120k | 144k | >=168k
2010,2011 and 2012 CH1: <=72k (20.54%) 96k (30.51%) 120k (25.55%) 144k (9.44%) >=168k (13.96%) N = 7735 | 0.9405 | 0.9449 | 0.9538 | 0.959 | 0.9645
% OPS spring | 0.19745 | 0.21638 | 0.22155 | 0.18114 | 0.18349
Chart: 
| <=72k | 96k | 120k | 144k | >=168k
2010,2011 and 2012 STH: <=72k (16.09%) 96k (30.08%) 120k (26.81%) 144k (11.28%) >=168k (15.74%) N = 8388 | 0.9521 | 0.9543 | 0.9589 | 0.9803 | 0.979
% OPS spring | 0.19745 | 0.21638 | 0.22155 | 0.18114 | 0.18349
Survival
%Time at Discharge
Survival
%Time at Discharge
Steelhead
Yearling Chinook

## Slide 53: Analyses: TDA Survival Grouped by Flow
Chart: 
| <=72k | 96k | 120k | 144k | >=168k
2010 and 2012 CH0: <=72k (10.50%) 96k (9.56%) 120k (53.25%) 144k (13.54%) >=168k (13.15%) N = 6760 | 0.8673 | 0.946 | 0.9527 | 0.9699 | 0.9531
% OPS summer | 0.2171 | 0.11405 | 0.43362 | 0.11414 | 0.1211
Subyearling Chinook
Survival
%Time at Discharge

## Slide 54: TDA Spillway

## Slide 55: Analyses: TDA Survival by Bay for All Years
Chart: 
| Bay 01 | Bay 02 | Bay 03 | Bay 04 | Bay 05 | Bay 06 | Bay 07 | Bay 08
2010, 2011 and 2012 CH1: Bay01 (6.63%) Bay02 (9.10%) Bay03 (9.18%) Bay04 (10.44%) Bay05 (11.53%) Bay06 (11.96%) Bay07 (13.37%) Bay08 (27.79%) N = 7736 | 0.9463 | 0.9251 | 0.9611 | 0.9536 | 0.9526 | 0.9486 | 0.9525 | 0.9535
count | 513 | 704 | 710 | 808 | 892 | 925 | 1034 | 2150
Survival
Yearling Chinook
Steelhead
Survival
Chart: 
| Bay 01 | Bay 02 | Bay 03 | Bay 04 | Bay 05 | Bay 06 | Bay 07 | Bay 08
2010, 2011 and 2012 STH: Bay01 (6.92%) Bay02 (8.67%) Bay03 (8.52%) Bay04 (9.38%) Bay05 (8.90%) Bay06 (11.68%) Bay07 (13.27%) Bay08 (32.66%) N = 8390 | 0.9578 | 0.9568 | 0.9656 | 0.979 | 0.9578 | 0.9661 | 0.9565 | 0.9603
count | 581 | 727 | 715 | 787 | 747 | 980 | 1113 | 2740

## Slide 56: Analyses: TDA Survival by Bay for All Years
Chart: 
| Bay 01 | Bay 02 | Bay 03 | Bay 04 | Bay 05 | Bay 06 | Bay 07 | Bay 08
2010 and 2012 CH0: Bay01 (6.07%) Bay02 (9.67%) Bay03 (11.09%) Bay04 (11.64%) Bay05 (12.32%) Bay06 (13.33%) Bay07 (12.78%) Bay08 (23.09%) N = 6760 | 0.9352 | 0.9519 | 0.952 | 0.9516 | 0.9465 | 0.9441 | 0.9464 | 0.9365
count | 410 | 654 | 750 | 787 | 833 | 901 | 864 | 1561
Survival
Sub-Yearling Chinook

## Slide 57: Analyses: TDA Survival by Flow, 2010, 2011, 2012
Chart: 
| <=70k | 80k | 90k | 100k | 110k | 120k | 130k | 140k | 150k | >=160k
2010,2011 and 2012 CH1: <=70k (10.55%) 80k (9.99%) 90k (6.49%) 100k (19.24%) 110k (11.51%) 120k (12.88%) 130k (7.28%) 140k (2.47%) 150k (4.33%) >=160k (15.27%) N = 7735 | 0.9364 | 0.9448 | 0.943 | 0.9439 | 0.9542 | 0.9532 | 0.954 | 0.9476 | 0.9675 | 0.9634
% OPS spring | 0.1218 | 0.075665 | 0.059666 | 0.1137 | 0.1057 | 0.11773 | 0.053857 | 0.053195 | 0.067003 | 0.23168
Survival
%Time at Discharge
Chart: 
| <=70k | 80k | 90k | 100k | 110k | 120k | 130k | 140k | 150k | >=160k
2010,2011 and 2012 STH: <=70k (9.17%) 80k (6.93%) 90k (6.04%) 100k (18.43%) 110k (12.77%) 120k (13.81%) 130k (7.14%) 140k (2.67%) 150k (5.20%) >=160k (17.85%) N = 8388 | 0.9548 | 0.9485 | 0.9349 | 0.9616 | 0.9583 | 0.9614 | 0.9484 | 0.9695 | 0.9839 | 0.9815
% OPS spring | 0.1218 | 0.075665 | 0.059666 | 0.1137 | 0.1057 | 0.11773 | 0.053857 | 0.053195 | 0.067003 | 0.23168
Survival
%Time at Discharge
Steelhead
Yearling Chinook

## Slide 58: Analyses: TDA Survival by Flow, 2010, 2011, 2012
Chart: 
| <=70k | 80k | 90k | 100k | 110k | 120k | 130k | 140k | 150k | >=160k
2010 and 2012 CH0: <=70k (4.41%) 80k (6.09%) 90k (4.64%) 100k (2.26%) 110k (6.89%) 120k (14.59%) 130k (36.04%) 140k (8.31%) 150k (2.25%) >=160k (14.51%) N = 6760 | 0.8305 | 0.8933 | 0.9362 | 0.9429 | 0.9598 | 0.9505 | 0.9535 | 0.9704 | 0.9671 | 0.9565
% OPS summer | 0.14757 | 0.069532 | 0.05365 | 0.033682 | 0.059027 | 0.12714 | 0.29759 | 0.071324 | 0.01484 | 0.12564
Sub-Yearling Chinook
Survival
%Time at Discharge

## Slide 59: TDA Egress

## Slide 60: TDA: CH1 Tailrace Egress Spillway
CH1 | SP24 | Min | Max | Mean | StdErr | Median | N
TR_EGR_TIME | 48 | 0.28 | 153.02 | 1.69 | 0.83 | 0.47 | 210
 | 72 | 0 | 367.24 | 1.14 | 0.35 | 0.36 | 1233
 | 96 | 0 | 475.07 | 2.14 | 0.69 | 0.27 | 858
 | 120 | 0.01 | 156.4 | 0.9 | 0.34 | 0.21 | 663
 | 144 | 0.1 | 120.33 | 0.49 | 0.26 | 0.16 | 464
 | 168 | 0.11 | 0.44 | 0.16 | 0 | 0.14 | 227
 | 312 | 0.14 | 0.14 | 0.14 | 0 | 0.14 | 2

## Slide 61: TDA: STH Tailrace Egress Spillway
STH | SP24 | Min | Max | Mean | StdErr | Median | N
TR_EGR_TIME | 48 | 0.27 | 201.79 | 1.63 | 1.05 | 0.42 | 192
 | 72 | 0 | 24.1 | 0.44 | 0.03 | 0.33 | 1060
 | 96 | 0 | 52.84 | 0.43 | 0.08 | 0.25 | 1006
 | 120 | 0 | 55.83 | 0.31 | 0.07 | 0.2 | 838
 | 144 | 0.1 | 3.81 | 0.21 | 0.01 | 0.15 | 610
 | 168 | 0.1 | 0.78 | 0.16 | 0 | 0.14 | 338
 | 312 | 0.14 | 0.14 | 0.14 | 0 | 0.14 | 2

## Slide 62: TDA: CH0 Tailrace Egress Spillway
CH0 | SP24 | Mean | StdErr | Min | Max | Mean | N
TR_EGR_TIME | 48 | 5.98 | 5.39 | 0.26 | 194.7 | 5.98 | 36
 | 72 | 0.73 | 0.15 | 0.16 | 65.88 | 0.73 | 560
 | 96 | 0.8 | 0.29 | 0.11 | 145.41 | 0.8 | 586
 | 120 | 0.57 | 0.13 | 0.12 | 324.61 | 0.57 | 3436
 | 144 | 0.84 | 0.42 | 0.11 | 324.19 | 0.84 | 870
 | 168 | 1.82 | 0.98 | 0.11 | 449.89 | 1.82 | 648
 | 216 | 18.26 | 12.55 | 0.17 | 324.49 | 18.26 | 36
 | 240 | 0.24 | 0.01 | 0.15 | 0.48 | 0.24 | 84
 | 312 | 0.18 | 0 | 0.12 | 0.54 | 0.18 | 168

## Slide 63: Conclusions: TDA
There was not a difference in survival of juvenile salmonids passing at spillbays 1-8 and spillbays 9-23
There was lower survival of CH0 at discharge below 72 kcfs